HY455 Cyber Security
Assignment 1
Chris Papastamos (csd4569)

1. Pawning SSIDs
For this task I created a hidden SSID from my home router that I could later pawn using kali linux:

In my laptop first of all I turned my wifi antenna into monitoring mode using the following three commands: $ sudo ifconfig wlan0 down; sudo iwconfig wlan0 mode monitor; sudo ifconfig wlan0 up

After that, using airodump-ng ($ airodump-ng wlan0) I captured the nearby networks, including one hidden with a SSID of 15 characters (This should the SSID I created).

Because there are a lot of results in airodump we will restart it showing only channel #1 SSIDs ($ airodump-ng –channel 1).For demonstration I will now connect my mobile phone to the hidden wifi network so that airodump can get the name and display it (this could also be done by deauthenticating an already connected station so that it tries to reconnect)

Here we can see the name of the hidden wifi:

And here my mobile phone exchanging packets with the station:

2. MAC spoofing
A MAC address is a static address for each interface of a device and for that reason the major way of recognizing a network device is through its MAC address. Therefore, a device which can change it’s MAC address can pretend to be another device.

MAC spoofing is the process of changing the MAC address of an interface. This is done for multiple reasons including impersonating other devices on a network or even avoiding filters of a router which clock or restrict access to a resource or the Internet. A commonly used tool in Kali linux is macchanger which allows a user to change an interface’s MAC address

For demonstration I will start by taking down the interface that I want to change its MAC. After I user macchanger -a wlan0 to change the MAC address and then take the interface up once again.